Field Observer Form for Quick Shoreline Assessment

1.

Shoreline Area Name:

|  | Zone | Division | Date: | Time: |
| --- | --- | --- | --- | --- |
| Segment ID or location description: |

Tidal Conditions (e.g.: high, falling)

GPS Coordinates (if available)

Surveyed by:  __Foot     __Boat

__Vehicle __Aircraft

Team I.D.

Name:                           for:

|  | Name: for: |
| --- | --- |

2. Any shoreline impact observed?  (circle)        Yes        No

3. If “Yes”, provide approximate length & width of impact.   Length ________   Width _______

4. Was oil observed in the nearby water? (circle)    Yes      No

If 2 and 4 are “No,”  STOP HERE.

5. Impacted Shoretypes & Materials

Check

| boxes below for all shore-types and materials present |  |
| --- | --- |
| marsh/swamp |
| tidal flat |
| riprap |
| sand or shell beach |
| clay bluff |
| dune |
| bulkhead, manmade structures |
| debris (trash, driftwood, etc.) |
| other vegetation |

6. Oil Condition 	__Fresh Oil     __Mousse     __Tarballs     __Tarpatties    __Tarmats    __Tar     __Asphalt

(Check all oil types present)		          	          (<10cm)	      (10-50cm)	    (>50cm)

7. Oiled Wildlife    Check any observed impacted wildlife   __birds    __fish    __invertebrates    __other?

(crabs, etc.)

8. Access Restrictions:

9. Cleanup Recommendations & Other Comments (make flagging notes here):

Caution: presence of marsh or tidal flat requires visit by SCAT prior to undertaking any cleanup action.

TGLO

# Text boxes

TRACE

<1%